ARUNAI ENGINEERING COLLEGE, TIRUVANNAMALAI – 3

DEPARTMENT OF COMPUTER SCIENCE AND ENGINEERING

TWO MARK QUESTIONS AND ANSWERS

SUBJECT    :  COMPUTER NETWORKS			             SEMESER: IV

SUB CODE:   CS1302							SECTION: A & B

PART A

UNIT – I

DATA COMMUNICATION

1. What is mean by data communication?

Data communication is the exchange of data (in the form of 1s and 0s) between two

devices via some form of transmission medium (such as a wire cable).

2. What are the three criteria necessary for an effective and efficient network?

The most important criteria are performance, reliability and security.

Performance of the network depends on number of users, type of transmission

medium, the capabilities of the connected h/w and the efficiency of the s/w.

Reliability is measured by frequency of failure, the time it takes a link to recover from

the failure and the network’s robustness in a catastrophe.

Security issues include protecting data from unauthorized access and viruses.

3. What are the three fundamental characteristics determine the effectiveness of

the data communication system?

The effectiveness of the data communication system depends on three fundamental

characteristics:

Delivery: The system must deliver data to the correct destination.

Accuracy: The system must deliver data accurately.

Timeliness: The system must deliver data in a timely manner.

4. What are the advantages of distributed processing?

Advantages of distributed processing include security/encapsulation, distributed

databases, faster problem solving, security through redundancy and collaborative

processing.

5. Why are protocols needed?

In networks, communication occurs between the entities in different systems. Two

entities cannot just send bit streams to each other and expect to be understood. For

communication, the entities must agree on a protocol. A protocol is a set of rules that

govern data communication.

6. Why are standards needed?

Co-ordination across the nodes of a network is necessary for an efficient

communication. If there are no standards, difficulties arise. A standard provides a model

or basis for development to which everyone has agreed.

7. For n devices in a network, what is the number of cable links required for a

mesh and ring topology?

Mesh topology – n (n-1)/2

Ring topology – n

8. What is the difference between a passive and an active hub?

An active hub contains a repeater that regenerates the received bit patterns before

sending them out. A passive hub provides a simple physical connection between the

attached devices.

2

9. Distinguish between peer-to-peer relationship and a primary-secondary

relationship.

Peer-to-peer relationship: All the devices share the link equally.

Primary-secondary relationship: One device controls traffic and the others must

transmit through it.

10. Assume 6 devices are arranged in a mesh topology. How many cables are

needed? How many ports are needed for each device?

Number of cables=n (n-1)/2=6(6-1)/2=15

Number of ports per device=n-1=6-1=5

11. Group the OSI layers by function.

The seven layers of the OSI model belonging to three subgroups. Physical, data link

and network layers are the network support layers; they deal with the physical aspects

of moving data from one device to another. Session, presentation and application layers

are the user support layers; they allow interoperability among unrelated software

systems. The transport layer ensures end-to-end reliable data transmission.

12. What are header and trailers and how do they get added and removed?

Each layer in the sending machine adds its own information to the message it

receives from the layer just above it and passes the whole package to the layer just

below it. This information is added in the form of headers or trailers. Headers are added

to the message at the layers 6,5,4,3, and 2. A trailer is added at layer2. At the receiving

machine, the headers or trailers attached to the data unit at the corresponding sending

layers are removed, and actions appropriate to that layer are taken.

13. The transport layer creates a communication between the source and

destination. What are the three events involved in a connection?

Creating a connection involves three steps: connection establishment, data transfer

and connection release.

14. What is the DC component?

Direct current is a zero-frequency signal with constant amplitude.

15. How does NRZ-L differ from NRZ-I?

In the NRZ-L sequence, positive and negative voltages have specific meanings:

positive for 0 and negative for 1. in the NRZ-I sequence, the voltages are meaningless.

Instead, the receiver looks for changes from one level to another as its basis for

recognition of 1s.

16. Using HDB3, encode the bit stream 10000000000100. Assume the number of 1s

so far is odd and the first 1 is positive.

17. What are the functions of a DTE? What are the functions of a DCE?

Data terminal equipment is a device that is an information source or an information

sink. It is connected to a network through a DCE.

Amplitude

Time

1 0 0 0 0 0 0 0 0 0 0 1 0 0

3

Data circuit-terminating equipment is a device used as an interface between a DTE and

a network.

18. What does the electrical specification of EIA-232 describe?

The electrical specification of EIA-232 defines that signals other than data must be

sent using OFF as less than -3 volts and ON as greater than +3 volts. The data must be

transmitted using NRZ-L encoding.

19. Discuss the mode for propagating light along optical channels.

There are two modes for propagating light along optical channels, multimode and

single mode.

Multimode: Multiple beams from a light source move through the core in different paths.

Single mode: Fiber with extremely small diameter that limits beams to a few angles,

resulting in an almost horizontal beam.

20. What is refraction?

The phenomenon related to the bending of light when it passes from one medium to

another.

UNIT-II

DATA LINK LAYER

1.What are the responsibilities of data link layer?

Specific responsibilities of data link layer include the following.

a) Framing

b) Physical addressing

c) Flow control

d) Error control

e) Access control

2. Mention the types of errors.

There are 2 types of errors

a) Single-bit error.

b) Burst-bit error.

3. Define the following terms.

Single bit error: The term single bit error means that only one bit of a given data unit

(such as byte character/data unit or packet) is changed from 1 to 0 or from 0 to 1.

Burst error: Means that 2 or more bits in the data unit have changed from 1 to 0 from

0 to 1.

4. What is redundancy?

It is the error detecting mechanism, which means a shorter group of bits or extra

bits may be appended at the destination of each unit.

5. List out the available detection methods.

There are 4 types of redundancy checks are used in data communication.

a) Vertical redundancy checks (VRC).

b) Longitudinal redundancy checks (LRC).

c) Cyclic redundancy checks (CRC).

d) Checksum.

6. Write short notes on VRC.

The most common and least expensive mechanism for error detection is the vertical

redundancy check (VRC) often called a parity check. In this technique a redundant bit

4

called a parity bit, is appended to every data unit so, that the total number of 0’s in the unit

(including the parity bit) becomes even.

7. Write short notes on LRC.

In longitudinal redundancy check (LRC), a block of bits is divided into rows and a

redundant row of bits is added to the whole block.

8. Write short notes on CRC.

The third and most powerful of the redundancy checking techniques is the cyclic

redundancy checks (CRC) CRC is based on binary division. Here a sequence of redundant

bits, called the CRC remainder is appended to the end of data unit.

9. Write short notes on CRC generator.

A CRC generator uses a modulo-2 division.

° In the first step, the 4-bit divisor is subtracted from the

first 4 bit of the

dividend.

° Each bit of the divisor is subtracted from the

corresponding bit of the

dividend without disturbing the next higher bit.

10. Write short notes on CRC checker.

A CRC checker functions exactly like a generator. After receiving the data appended

with the CRC it does the same modulo-2 division. If the remainder is all 0’s the CRC is

dropped and the data accepted. Otherwise, the received stream of bits is discarded and the

dates are resent.

11. Give the essential properties for polynomial.

A polynomial should be selected to have at least the following properties.

a) It should not be

b) It should be divisible by(x+1).

12. Define checksum.

The error detection method used by the higher layer protocol is called checksum.

Checksum is based on the concept of redundancy.

13. What are the steps followed in checksum generator?

The sender follows these steps

a) The units are divided into k sections each of n bits.

b) All sections are added together using 2’s complement to get the sum.

c) The sum is complemented and become the checksum.

d) The checksum is sent with the data.

14. List out the steps followed is checksum checker side.

The receiver must follow these steps

a) The unit is divided into k section each of n bits.

b) All sections are added together using 1’s complement to get the sum.

c) The sum is complemented.

d) If the result is zero.

15. Write short notes on error correction.

It is the mechanism to correct the errors and it can be handled in 2 ways.

a) When an error is discovered, the receiver can have the sender

retransmit the entire data unit.

b) A receiver can use an error correcting coder, which automatically

corrects certain errors.

5

16. Mention the types of error correcting methods.

There are 2 error-correcting methods.

a) Single bit error correction

b) Burst error correction.

17. What is the purpose of hamming code?

A hamming code can be designed to correct burst errors of certain lengths. So the

simple strategy used by the hamming code to correct single bit errors must be redesigned

to be applicable for multiple bit correction.

18. Define flow control.

Flow control refers to a set of procedures used to restrict the amount of data. The

sender can send before waiting for acknowledgment.

19. What is a buffer?

Each receiving device has a block of memory called a buffer, reserved for storing

incoming data until they are processed.

20. Mention the categories of flow control.

There are 2 methods have been developed to control flow of data across

communication links.

a) Stop and wait- send one from at a time.

b) Sliding window- send several frames at a time.

UNIT III

NETWORK LAYER

1. What are the network support layers and the user support layers?

Network support layers:

The network support layers are Physical layer, Data link layer and Network layer. These

deals with electrical specifications, physical connection, transport timing and reliability.

User support layers:

The user support layers are: Session layer, Presentation layer, Application layer. These

allow interoperability among unrelated software system.

2. With a neat diagram explain the relationship of IEEE Project to the OSI model?

The IEEE has subdivided the data

link layer into two sub layers:

* Logical link control (LLC)

* Medium access control (MAC)

LLC is non-architecture specific. The MAC sub layer contains a number of distinct

modules, each carries proprietary information specific to the LAN product being used.

3. What are the functions of LLC?

The IEEE project 802 models takes the structure of an HDLC frame and divides it

into 2 sets of functions. One set contains the end user portion of the HDLC frame - the

Other layers

Network

Data link

Physical

Other layers

Network

Logical Link Control

Media Access Control

Physical

6

logical address, control information, and data. These functions are handled by the IEEE

802.2 logical link control (LLC) protocol.

4. What are the functions of MAC?

MAC sub layer resolves the contention for the shared media. It contains

synchronization, flag, flow and error control specifications necessary to move information

from one place to another, as well as the physical address of the next station to receive and

route a packet.

5. What is protocol data unit?

The data unit in the LLC level is called Protocol Data Unit (PDU). It contains four

fields.

• Destination Service Point Address (DSAP)

• Source Service Access Point

• Control field

• Information field

6. What are headers and trailers and how do they get added and removed?

The control data added to the beginning of a data is called headers. The control data

added to the end of a data is called trailers. At the sending machine, when the message

passes through the layers each layer adds the headers or trailers. At the receiving machine,

each layer removes the data meant for it and passes the rest to the next layer.

7. What are the responsibilities of network layer?

The network layer is responsible for the source-to-destination delivery of packet across

multiple network links. The specific responsibilities of network layer include the following:

• Logical addressing.

• Routing.

8. What is a virtual circuit?

A logical circuit made between the sending and receiving computers. The connection

is made after both computers do handshaking. After the connection, all packets follow the

same route and arrive in sequence.

9. What are data grams?

In datagram approach, each packet is treated independently from all others. Even

when one packet represents just a place of a multipacket transmission, the network treats it

although it existed alone. Packets in this technology are referred to as datagram.

10. What are the two types of implementation formats in virtual circuits?

Virtual circuit transmission is implemented in 2 formats.

• Switched virtual circuit

• Permanent virtual circuit.

11. What is meant by switched virtual circuit?

Switched virtual circuit format is comparable conceptually to dial-up line in

circuit switching. In this method, a virtual circuit is created whenever it is needed and exits

only for the duration of specific exchange.

12. What is meant by Permanent virtual circuit?

Permanent virtual circuits are comparable to leased lines in circuit switching.

In this method, the same virtual circuit is provided between two uses on a continuous basis.

The circuit is dedicated to the specific uses.

13. Define Routers.

DSAP SSAP Control Information

7

Routers relay packets among multiple interconnected networks. They Route packets

from one network to any of a number of potential destination networks on Internet routers

operate in the physical, data link and network layer of OSI model.

14. What is meant by hop count?

The pathway requiring the smallest number of relays, it is called hop-count routing, in

which every link is considered to be of equal length and given the value one.

15. How can the routing be classified?

The routing can be classified as,

• Adaptive routing

• Non-adaptive routing.

16. What is time-to-live or packet lifetime?

As the time-to-live field is generated, each packet is marked with a lifetime, usually

the number of hops that are allowed before a packet is considered lost and accordingly,

destroyed. The time-to-live determines the lifetime of a packet.

17. What is meant by brouter?

A brouter is a single protocol or multiprotocol router that sometimes act as a router

and sometimes act as a bridge.

18. Write the keys for understanding the distance vector routing.

The three keys for understanding the algorithm are

• Knowledge about the whole networks

• Routing only to neighbors

• Information sharing at regular intervals

19. Write the keys for understanding the link state routing.

The three keys for understanding the algorithm are

• Knowledge about the neighborhood.

• Routing to all neighbors.

• Information sharing when there is a range.

20. How the packet cost referred in distance vector and link state routing?

In distance vector routing, cost refer to hop count while in case of link state routing, cost is a

weighted value based on a variety of factors such as security levels, traffic or the state of

the link.

UNIT IV

TRANSPORT LAYER

1. What is function of transport layer?

The protocol in the transport layer takes care in the delivery of data from one

application program on one device to an application program on another device.

They act as a link between the upper layer protocols and the services provided by

the lower layer.

2. What are the duties of the transport layer?

The services provided by the transport layer

End-to- end delivery

Addressing

Reliable delivery

Flow control

Multiplexing

8

3. What is the difference between network layer delivery and the transport layer

delivery?

Network layer delivery Transport layer delivery

The network layer is responsible

for the the source-to-destination

delivery of packet

across multiple network links.

The transport layer is responsible

for source-to-destination delivery

of the entire message.

4. What are the four aspects related to the reliable delivery of data?

The four aspects are,

Error control

Sequence control

Loss control

Duplication control

5. What is meant by segment?

At the sending and receiving end of the transmission, TCP divides long

transmissions into smaller data units and packages each into a frame called a segment.

6. What is meant by segmentation?

When the size of the data unit received from the upper layer is too long for the

network layer datagram or data link layer frame to handle, the transport protocol divides

it into smaller usable blocks. The dividing process is called segmentation.

7. What is meant by Concatenation?

The size of the data unit belonging to single sessions are so small that several

can fit together into a single datagram or frame, the transport protocol combines them

into a single data unit. The combining process is called concatenation.

8. What are the types of multiplexing?

The types of multiplexing are,

Upward multiplexing

Downward multiplexing

9. What are the two possible transport services?

Two basic types of transport services are,

Connection service

Connectionless services

10. The transport layer creates the connection between source and destination.

What are the three events involved in the connection?

For security, the transport layer may create a connection between the two end

ports. A connection is a single logical path between the source and destination that

is associated with all packets in a message. Creating a connection involves three

steps:

• Connection establishment

• Data transfer & Connection release.

11. What is meant by congestion?

Congestion in a network occurs if user sends data into the network at a rate

greater than that allowed by network resources.

12. Why the congestion occurs in network?

9

Congestion occurs because the switches in a network have a limited buffer size

to store arrived packets.

13. What is meant by quality of service?

The quality of service defines a set of attributes related to the performance of the

connection. For each connection, the user can request a particular attribute each

service class is associated with a set of attributes.

14. What are the two categories of QoS attributes?

The two main categories are

User Oriented

Network Oriented

15. List out the user related attributes?

User related attributes are

SCR – Sustainable Cell Rate

PCR – Peak Cell Rate

MCR- Minimum Cell Rate

CVDT – Cell Variation Delay Tolerance

16. What are the networks related attributes?

The network related attributes are,

Cell loss ratio (CLR)

Cell transfer delay (CTD)

Cell delay variation (CDV)

Cell error ratio (CER)

17. What is the difference between service point address, logical address and

physical address?

Service point

addressing

Logical addressing Physical addressing

The transport layer

header includes a type of

address called a service

point address or port

address, which makes a

data delivery from a

specific process on one

computer to a specific

process on another

computer.

If a packet passes the

network boundary we

need another addressing

to differentiate the source

and destination systems.

The network layer adds a

header, which indicate

the logical address of the

sender and receiver.

If the frames are to be

distributed to different

systems on the network,

the data link layer adds

the header, which defines

the source machine’s

address and the

destination machine’s

address.

17. What are the rules of nonboundary-level masking?

• The bytes in the IP address that corresponds to 255 in the mask will be

repeated in the subnetwork address

• The bytes in the IP address that corresponds to 0 in the mask will

change to

0 in the subnetwork address

• For other bytes, use the bit-wise AND operator

19. Define Gateway.

A device used to connect two separate networks that use different communication

protocols.

10

20. What is LSP?

In link state routing, a small packet containing routing information sent by a router to

all other router by a packet called link state packet.

UNIT – V

APPLICATION LAYER

1. What is the purpose of Domain Name System?

Domain Name System can map a name to an address and conversely an

address to name.

2. Discuss the three main division of the domain name space.

Domain name space is divided into three different sections: generic domains,

country domains & inverse domain.

Generic domain: Define registered hosts according to their generic behavior, uses

generic suffixes.

Country domain: Uses two characters to identify a country as the last suffix.

Inverse domain: Finds the domain name given the IP address.

3. Discuss the TCP connections needed in FTP.

FTP establishes two connections between the hosts. One connection is used for

data transfer, the other for control information. The control connection uses very simple

rules of communication. The data connection needs more complex rules due to the

variety of data types transferred.

4. Discuss the basic model of FTP.

The client has three components: the user interface, the client control process,

and the client data transfer process. The server has two components: the server control

process and the server data transfer process. The control connection is made between

the control processes. The data connection is made between the data transfer

processes.

5. What is the function of SMTP?

The TCP/IP protocol supports electronic mail on the Internet is called Simple Mail

Transfer (SMTP). It is a system for sending messages to other computer users based

on e-mail addresses. SMTP provides mail exchange between users on the same or

different computers.

6. What is the difference between a user agent (UA) and a mail transfer agent

(MTA)?

The UA prepares the message, creates the envelope, and puts the message in

the envelope. The MTA transfers the mail across the Internet.

7. How does MIME enhance SMTP?

MIME is a supplementary protocol that allows non-ASCII data to be sent through

SMTP. MIME transforms non-ASCII data at the sender site to NVT ASCII data and

deliverers it to the client SMTP to be sent through the Internet. The server SMTP at the

receiving side receives the NVT ASCII data and delivers it to MIME to be transformed

back to the original data.

8. Why is an application such as POP needed for electronic messaging?

Workstations interact with the SMTP host, which receives the mail on behalf of

every host in the organization, to retrieve messages by using a client-server protocol

such as Post Office Protocol, version 3(POP3). Although POP3 is used to download

11

messages from the server, the SMTP client still needed on the desktop to forward

messages from the workstation user to its SMTP mail server.

9. Give the format of HTTP request message.

10. Give the format of HTTP response message.

11. Write down the three types of WWW documents.

The documents in the WWW can be grouped into three broad categories: static,

dynamic and active.

Static: Fixed-content documents that are created and stored in a server.

Dynamic: Created by web server whenever a browser requests the document.

Active: A program to be run at the client side.

12. What is the purpose of HTML?

Status Line

Headers

A Blank Line

Body

(present only in

some messages)

Request Line

Headers

A Blank Line

Body

(present only in

some messages)

12

HTML is a computer language for specifying the contents and format of a web

document. It allows additional text to include codes that define fonts, layouts, embedded

graphics and hypertext links.

13. Define CGI.

CGI is a standard for communication between HTTP servers and executable

programs. It is used in crating dynamic documents.

14. Name four factors needed for a secure network.

Privacy: The sender and the receiver expect confidentiality.

Authentication: The receiver is sure of the sender’s identity and that an imposter has

not sent the message.

Integrity: The data must arrive at the receiver exactly as it was sent.

Non-Reputation: The receiver must able to prove that a received message came from

a specific sender.

15. How is a secret key different from public key?

In secret key, the same key is used by both parties. The sender uses this key and

an encryption algorithm to encrypt data; the receiver uses the same key and the

corresponding decryption algorithm to decrypt the data.

In public key, there are two keys: a private key and a public key. The private key

is kept by the receiver. The public key is announced to the public.

16. What is a digital signature?

Digital signature is a method to authenticate the sender of a message. It is similar

to that of signing transactions documents when you do business with a bank. In network

transactions, you can create an equivalent of an electronic or digital signature by the

way you send data.

17. What are the advantages & disadvantages of public key encryption?

Advantages:

a) Remove the restriction of a shared secret key between two entities. Here each entity

can create a pair of keys, keep the private one, and publicly distribute the other one.

b) The no. of keys needed is reduced tremendously. For one million users to

communicate, only two million keys are needed.

Disadvantage:

If you use large numbers the method to be effective. Calculating the cipher text using

the long keys takes a lot of time. So it is not recommended for large amounts of text.

18. What are the advantages & disadvantages of secret key encryption?

Advantage:

Secret Key algorithms are efficient: it takes less time to encrypt a message. The reason

is that the key is usually smaller. So it is used to encrypt or decrypt long messages.

Disadvantages:

a) Each pair of users must have a secret key. If N people in world want to use this

method, there needs to be N (N-1)/2 secret keys. For one million people to

communicate, a half-billion secret keys are needed.

b) The distribution of the keys between two parties can be difficult.

19. Define permutation.

Permutation is transposition in bit level.

Straight permutation: The no. of bits in the input and output are preserved.

Compressed permutation: The no. of bits is reduced (some of the bits are dropped).

Expanded permutation: The no. of bits is increased (some bits are repeated).

13

20. Define substitutional & transpositional encryption.

Substitutional: A character level encryption in which each character is replaced by

another character in the set.

Transpositional: A Character level encryption in which the characters retain their

plaintext but the position of the character changes.

PART B

UNIT I

Data communications

1. Explain ISO/OSI reference model.

Physical layer

Data link layer

Network layer

Transport layer

Session layer

Presentation layer

Application layer

2. Explain the topologies of the network.

Mesh topology

Star topology

Tree topology

Bus topology

Ring topology

3. Explain the categories of networks.

Local Area Network(LAN)

Metropolitan Area Network(MAN)

Wide Area Network(WAN)

4. Explain coaxial cable & fiber optics.

Coaxial cable

Coaxial cable standards

Coaxial cable connectors

Fiber optics

Propagation modes

Fiber sizes

Cable composition

Light sources for optical cable

Fiber optic connectors

Advantages & disadvantages of optical fiber

5. Explain line coding (digital to digital conversion).

Unipolar

DC component

Synchronization

Polar

Non return to zero(NRZ)

NRZ-L

NRZ-I

14

Return to zero

Biphase

Manchester

Differential Manchester

Bipolar

Alternate Mark Inversion(AMI)

Bipolar 8-zero substitution(B8ZS)

High-Density Bipolar 3(HDB3)

UNIT II

Data link layer

1. Explain error detection and error correction techniques.

Types of errors

Single bit error

Burst error

Error detection

Vertical redundancy check(VRC)

Longitudinal redundancy check(LRC)

Cyclic redundancy check(CRC)

Checksum

Error correction

Single-bit error correction

Hamming code

Burst error correction

2. Explain error control mechanism.

Stop and wait ARQ

Sliding window ARQ

Go back-n

Selective-reject

3. Explain the flow control mechanism

Stop and wait

Sliding window.

4. Explain the timers and time registers in FDDI.

Time registers

Synchronous allocation(SA)

Target token rotation time(TTRT)

Absolute maximum time(AMT)

Timers

Token rotation timer(TRT)

Token holding timer(THT)

5. Explain about Ethernet.

Access method :CSMA/CD

Addressing

Electrical specification

Frame format

Implementation:

15

10 base 5 :Thick Ethernet

10 base 2 :Thin Ethernet

10 base T :Twisted-pair Ethernet

1 base 5 :Star LAN

UNIT III

Network layer

1. Explain the two approaches of packet switching techniques.

Datagram approach

Virtual circuit approach

Switched virtual circuit(SVC)

Permanent virtual circuit(PVC)

Circuit – switched connection versus virtual – circuit connection

Path versus route

Dedicated versus shared

2. Explain IP addressing method.

Internetwork protocol (IP)

Datagram

Addressing

Classes

Dotted decimal notation

A sample internet

3. Define routing & explain distance vector routing and link state routing.

Distance vector routing

Sharing information

Routing table

Creating the table

Updating the table

Updating algorithm

Link state routing

Information sharing

Packet cost

Link state packet

Getting information about neighbors

Initialization

Link state database

4. Define bridge and explain the type of bridges.

Bridges

Types of bridges

Simple bridge

Multiport bridge

Transparent bridge

5. Explain subnetting

Subnetting

Three levels of hierarchy

Masking

Masks without subnetting

16

Masks with subnetting

Finding the subnetwork address

Boundary level masking

Non-boundary level masking

UNIT IV

Transport layer

1. Explain the duties of transport layer.

End to end delivery

Addressing

Reliable delivery

• Error control

• Sequence control

• Loss control

• Duplication control

Flow control

Multiplexing

2. Explain socket in detail.

• Introduction

• Explanation

• program

3. Explain UDP & TCP.

User Datagram Protocol(UDP)

Source port address

Destination port address

Total length

Checksum

Transmission Control Protocol(TCP)

Source port address

Destination port address

Sequence number

Acknowledgement number

Header length

Reserved

Control

Window size

Check sum

Urgent pointer

Options and padding

4. Explain about congestion control.

Congestion avoidance

BECN

FECN

Four situations

Discarding

5. Explain leaky bucket and token bucket algorithm

Leaky bucket algorithm

17

Leaky bucket

Switch controlling the output rate

Flowchart

UNIT V

Application Layer

1. Explain the functions of SMTP.

• System for sending messages to other computer users based on e-mail

addresses. SMTP provides mail exchange between users on the same or

different computers.

• User Agent

• Mail Transfer Agent

• Multipurpose Internet Mail Extensions

• Post Office Protocol

2. Write short notes on FTP.

• Transfer a file from one system to another.

• TCP connections

• Basic model of FTP

3. Explain about HTTP.

• HTTP transactions

• HTTP messages

• URL

4. Explain the WWW in detail.

• Hypertext & Hypermedia

• Browser Architecture

• Categories of Web Documents

• HTML

• CGI

• Java

5. Explain the type of encryption/decryption method.

Conventional Methods:

• Character-Level Encryption: Substitutional & Transpositional

• Bit-Level Encryption: Encoding/Decoding, Permutation, Substitution, Product,

Exclusive-Or & Rotation

Public key Methods